## Slide 1
FOWLIE, PETERSEN & REGUANT (2021) — BORDER CARBON ADJUSTMENTS WHEN CARBON INTENSITY VARIES ACROSS PRODUCERS
eGRID Calibration Replication
An independent replication of the paper's eGRID2018 thermal-plant calibration step, with original follow-on analysis of regional carbon-intensity patterns.
Independent study · August 2026

## Slide 2
Replication Methodology
Original eGRID Script
Ran the original authors’ eGRID cleaning script against the public EPA eGRID2018 dataset to produce a plant-level thermal generator table.
Independent Analysis
Built five original outputs using Python (pandas, numpy), with AI-assisted coding (Claude).
Deliverables
Regional summary statistics, a generation-weighted regional average, and a fuel-type decomposition.
Original eGRID2018 cleaning script © Fowlie, Petersen & Reguant (openICPSR DOI 10.3886/E131024V1). All analysis beyond that step is independent work.
2

## Slide 3
Plant Counts & Rate Distribution
lb/MWh measures how much CO₂ is released per unit of electricity actually produced.
Region | Plants | Mean (lb/MWh) | Median (lb/MWh) | Max (lb/MWh)
California | 577 | 1650.1 | 905.9 | 122,001.9
Northwest | 253 | 1568.8 | 1207.5 | 12,221.8
Southwest | 283 | 1136.8 | 1015.3 | 4,559.7
Rockies | 189 | 1706.9 | 1176.1 | 9,121.6
Four WECC regions: California, Northwest, Southwest, and Rockies (plus a small unmatched bucket, excluded here).
Rockies
has the highest MEAN rate
But Northwest has the highest MEDIAN — Rockies’ average is skewed upward by a handful of extreme outliers.
3

## Slide 4
Outlier Drill-Down
122,001.9
lb/MWh — the most extreme rate in the dataset
A real-world data characteristic of idle peaker plants — not a data-pipeline error.
County | Fuel | Capacity (MW) | Generation (MWh) | Rate (lb/MWh)
Stanislaus | GAS | 24.9 | 5.0 | 122,001.9
Stanislaus | GAS | 24.9 | 5.0 | 122,001.9
San Bernardino | GAS | 1.2 | 8.0 | 16,333.4
This 24.9 MW gas plant in Stanislaus County generated just 5.0 MWh across the entire year — a capacity factor near zero. This is characteristic of a peaker plant, which runs only during rare, high-demand events (e.g., a heat wave).
Dividing its (relatively small) emissions by this near-zero generation inflates the rate — the plant isn’t unusually dirty, it simply produced very little electricity to divide by.
4

## Slide 5
Generation-Weighted vs. Simple Average
Region | Weighted avg (tonnes CO₂/MWh) | Paper reference point
California | 0.437 | CA default import rate: 0.428
Southwest | 0.685 | Paper: nonbaseload intensity “above 0.7”
Rockies | 0.828 | Paper: nonbaseload intensity “above 0.7”
Northwest | 0.781 | —
0.437 vs. 0.428
California’s weighted average vs. the state’s own regulatory default import rate
A reassuring, if coincidental, magnitude check — California’s default rate was calibrated from different (2006–2008, out-of-state) data.
Rockies (0.828) and Southwest (0.685) are broadly consistent with the paper’s claim that nonbaseload intensities exceed 0.7 in these regions; Southwest falls just under this threshold, likely because our calculation includes all thermal plants, not only nonbaseload ones.
California’s fossil-fuel fleet has a meaningfully lower carbon intensity than its neighbors — driven by its heavier reliance on gas over coal.
5

## Slide 6
Fuel-Type Composition by Region
Chart: Total Generation by Fuel Type (MWh)
| California | Northwest | Southwest | Rockies
Gas (MWh) | 88912696 | 45596811 | 67001781 | 16338939
Coal (MWh) | 8793545 | 63072487 | 44335727 | 29543672
California relies overwhelmingly on gas (89M MWh vs. 8.8M MWh coal) — the highest gas share of any region. In California specifically, gas and coal have similar per-plant emission rates; in every other region, coal is markedly dirtier than gas.
Region | Fuel | Mean rate (lb/MWh)
California | GAS | 1646.6
California | COAL | 1588.0
Rockies | GAS | 1496.3
Rockies | COAL | 2476.8
California: comparable rates by fuel. Rockies: coal far dirtier than gas — the more typical pattern.
6

## Slide 7
Scope & Limitations
eGRID’s thermal dataset excludes renewable and zero-carbon sources — solar, wind, hydro, and nuclear.
This analysis measures the carbon intensity of each region’s fossil-fuel fleet specifically, not its overall electricity mix.
A region with a dirtier thermal fleet could still have a cleaner overall grid if it draws more of its power from renewables.
Full findings, code, and data: github.com/jackcghu/wecc-bca-egrid-replication